## Slide 1: Internet of Things

## Slide 2: How do devices communicate?

## Slide 3: Serial Communication
Send data bit by bit
Format and transfer rate must be agreed at both ends

## Slide 4: HTTP

## Slide 5: HTTP: RESTful
A “request” is sent to a server via URL
  Eg. http://api.example.com/resources/user/1036721?name=something
Response is usually text in HTML, XML, or JSON
Great if your asking for something
  What about “push”
  Eg. Server wants to tell device to do something
Path or variables
variables

## Slide 6: HTTP: RESTful Hypothetical Light Switch
Server
Cell Phone
api.example.com/turnoff
WiFi Switch
Should I turn off?
Process Response
Turn off
No
Yes
api.example.com/shoulditurnoff

## Slide 7: MQTT: Message Queuing Telemetry Transport

## Slide 8: MQTT
MQTT was invented by Andy Stanford-Clark (IBM) and Arlen Nipper (Arcom, now Cirrus Link) back in 1999, when their use case was to create a protocol for minimal battery loss and minimal bandwidth connecting oil pipelines over satellite connection. They specified the following goals, which the future protocol should have:
  Simple to implement
  Provide a Quality of Service Data Delivery
  Lightweight and Bandwidth Efficient
  Data Agnostic
  Continuous Session Awareness

## Slide 9: MQTT: Pub/Sub
Clients connect to a “Broker”
Clients subscribe to topics eg,
  client.subscribe(‘toggleLight/1’)
  client.subscribe(‘toggleLight/2’)
  client.subscribe(‘toggleLight/3’)
Clients can publish messages to topics:
  client.publish(‘toggleLight/1’, ‘toggle’);
  client.publish(‘toggleLight/2’, ‘toggle’);
All clients receive all messages published to topics they subscribe to
Messages can be anything
  Text
  Images
  etc

## Slide 10: MQTT Hypothetical Light Switch
Broker
Cell Phone
client.publish(‘lightSwitch/1’, ‘toggle’)
WiFi Switch
Toggle Switch
‘toggle’

## Slide 11: Websockets
Chrome supports HTTP, HTTPS, FILE, FTP, WS (websockets).
Chrome does not support MQTT
But you can do MQTT over websockets!
What is websockets?

## Slide 12: Websockets

## Slide 13: Websockets
var webSocketServer = require('ws').Server;
var wss = new webSocketServer({port: 8080});
// broadcast client message to all
wss.broadcast = function broadcast(data) {
wss.clients.forEach(function each(client) {
client.send(data);
});
};
// catch client messages
wss.on('connection', function connection(ws) {
ws.on('message', function incoming(message) {
console.log('received from %s', message);
wss.broadcast(message);
});
});
var webSocketClient = require('ws');
var ws = new webSocketClient('ws://localhost:8080');
var id = Math.floor(Math.random()*10000);
ws.on('message', function(message) {
console.log('received from %s', message);
});
function sendMessage(){
var timeStamp = Date.now();
var message = 'clientId:' + id + ', '
+ 'timeStamp:' + timeStamp;
ws.send(message);
}
function timer(){
sendMessage();
setTimeout(timer, 3000);
}
ws.on('open', function() {
timer();
});
server.js
client.js

## Slide 14: MQTT Over Websockets
We can still use MQTT in a browser
The connection is handled via Websockets
This eliminates a lot of the “housekeeping” required by Websockets
Many to many communication much easier

## Slide 15: MQTT
var mqtt = require('mqtt')
client = mqtt.connect('mqtt://162.243.219.88',1883)
client.on('message', function (topic, message) {
console.log(message)
});
client.on('connect', function () {
client.subscribe('tesselData');
client.publish('tesselData','Hello from <someone>')
});

## Slide 16: MQTT in the wild

## Slide 17: The Broker
IP Address: 162.243.219.88
MQTT Port: 1883 (For running in NodeJS)
Websocket Port: 9001 (For running in a web browser)
Broker is running on DigitalOcean
  https://www.digitalocean.com/
Broker is Mosquitto
  https://mosquitto.org/

## Slide 18: Active Learning
mqtt-formatting
  Connect to an MQTT server
  Send and receive messages

## Slide 19: Channels in MQTT
Channels/topics in MQTT work like file paths
When subscribing to a channel we have to specify the whole path
Or use a wildcard
  +
  #

## Slide 20: + Wildcard

## Slide 21: # Wildcard

## Slide 22: Active Learning
mqtt-channels
  Understand how channel paths work

## Slide 23: MQTT Light Switch
browser-hardware-matrix.zip
Use MQTT to send a message to the device to toggle an LED
  Format as JSON string
    {id:”YourID”, state:true/false}
  Your ID is the day of your birthday plus by 0 (male) or 32 (female)
  John was born on the 27th February, his ID is 27.
  Elizabeth was born on 11th May, her ID is 43
Add your code to ledMatrix.html to send the message
serverTessel.js is the code running on the device

## Slide 24: Chat with MQTT
chat.zip on stellar

## Slide 25: Plotting Ambient Sensor Data
Browser-hardware-sensors.zip
Add your code to sensors.html
Receive sensor data via MQTT
  Format as a JSON string:
    {date, lightLevel:data, soundLevel:data}
Plot the data live with google charts
serverTessel.js is the code running on the device

## Slide 26: Timestamps
How do we know the order in which events occurred?
Messages might be timestamped
  Were the clocks synced across machines?
Ultimate solution:
  https://en.wikipedia.org/wiki/Spanner_(database)